# ABANAKI

## OIL GRABBER( SKIMMER

#### MODEL 8(

### Installation and Maintenance Instructions

Your Abanaki Oil Grabber( Model 8( is shipped in four packages:

- Base Unit

- Tail Pulley

- Motor

- Belt

Step 1. MOUNTING THE BASE UNIT.

Although the Oil Grabber can be put on any part of the tank, it is best positioned where the bulk of the oil is accumulating.

CHANNEL MOUNT: (SEE FIG. 1)

Use 5” channel (C5x6.7).

- Prepare your 5” channel by sealing the channel opening opposite the discharge end.

- Mount your channel where the skimmer will operate. The channel should have a slope of 1 or 2 degrees to allow oil to discharge smoothly into a disposal tank.

- Locate the support gusset and the channel mount clamp on the bottom of the unit and remove the three bolts.

- Position the channel mount clamp on the channel as desired. Set the base unit on top of channel mount clamp.

- Place the support gusset up and under the channel with the adjusting cam inserted in its proper position.

- Replace the (3) bolts removed in step C and put light tension on them. Do not tighten until final belt adjustment is made. (Step 12)

FLAT MOUNT: (Optional) (SEE FIG. 2)

Mounting surface should be level.

- Disassemble the base mounting assembly, flat mount trough and flat mount plate, noting the position of all bolts, nuts, and washers, as well as the adjustment cam.

- Drill four ½” clearance holes in mounting surface (matching those on the flat mount plate) and securely bolt the flat mount plate in place.

- Assemble base assembly and flat mount trough on top of flat mount plate making sure to reinsert the adjusting cam in its correct position.

- Replace the bolts removed putting light tension on the (3) bolts holding the main base to the flat mount plate. Do not tighten until final belt adjustment is made. (Step 12)

FLOOR STAND OPTION: If mounting on floor stand, follow separate instructions enclosed.

Step 2. Remove the guard over the head pulley by lifting straight up.

Step 3. Locate the adjustable wiper assembly on the outside trough and loosen the locknut. Turn adjusting screw clockwise until wiper is completely open. (SEE FIG. 3)

Step 4. Unpack the belt carefully following the directions in the carton.

- When handling metal belts wear cloth gloves.

- Dents or creases can cause premature wear.

Step 5. Insert the belt between the troughs, lifting the belt over onto the head pulley between the head pulley flanges. (SEE FIG. 4)

Step 6. (SEE FIG. 5) If you have purchased the Yoke and Tether option continue with step 7. If you have purchased the “Tail Pulley-Retainer-Belt Assembly” option follow those instructions enclosed and continue with step 9. If neither of these options apply, continue with step 8. Note: Whichever option you have, the tail pulley must be fully submerged below the surface.

Step 7. Place an “S” hook through the hole on the inside support angle, (SEE FIG. 5) and hook the last link of the chain onto the bottom loop of the “S” hook. Lower the tail pulley into the belt. The tail pulley is supported by the belt, not the chain. Make certain that the belt is taut by the weight of the tail pulley and that the chain is loose by two links. Note: Tail pulley must be fully submerged below the surface. Continue with step 10.

Step 8. Gently pull up the belt until the bottom is slightly above the surface. Place the tail pulley in the belt and slowly lower the belt, (taking care not to dislodge the tail pulley), until the belt is once again taut and the tail pulley is fully submerged below the surface. Continue with step 10.

Step 9. Place an “S” hook through the hole on the inside support angle, (SEE FIG. 5) and hook the last link of the chain onto the bottom loop of the “S” hook. Lower the “Tail Pulley-Retainer-Belt Assembly” into the tank. The tail pulley is supported by the belt, not the chain. Make certain that the belt is taut by the weight of the tail pulley and that the chain is loose  by two links. Note: Tail pulley must be fully submerged below the surface.

Step 10. Carefully turn the adjustment screw on the adjustable wiper blade so that the blade is gently touching the belt with even contact for the length of the blade. Do not set blade too tight. This could reduce the life expectancy of the belt. After this adjustment, tighten locknut securely.

Step 11.

- Remove the plastic protective plug from the gear reducer top and replace with breather plug supplied. (SEE FIG. 6)

- Motor/Gear Reducer Key Installation:

NOTE: Do Not use key provided with motor. Use only key provided with gear reducer.

- Place key FLUSH with end of motor shaft.

- Carefully insert motor shaft into gear reducer. DO NOT FORCE.

- If motor and gear reducer do not easily slide together, the key is binding. Repeat steps 1 & 2.

- Bolt motor to gearbox with four bolts and lock washers provided.

- Connect motor leads to power so that the belt is carried downward through the wiper blades. (Rotation is in direction of the red arrow on the back of the base unit) (SEE FIG. 6).

Step 12. Leveling the Belt (SEE FIG. 7)

Be sure the unit is as level as possible. Unit should not be tilted side to side, nor front to rear. Turn motor on and observe the unit. The belt should run without rubbing on the flanges of the head pulley. If the belt is rubbing, unit can be adjusted by turning the leveling cam located on the inside bottom of the inboard plate (SEE FIG. 7). The cam must be turned slowly, and observe the belt after each 1/16th of a turn.

After belt is running smoothly between the head pulley flanges, tighten down the three mounting bolts on the channel mount clamp (channel mount) or the flat mount plate (flat mount).

Step 13. Place the guard back into place.

GENERAL MAINTENANCE

- Check magnetized head pulley for buildup of any metallic parts and clean if necessary.

- Clean or flush discharge hose and discharge troughs to remove accumulated sludge or waste.

- Check belt condition for evidence of wear or cracks and replace if necessary. Make certain belt is running near center of head pulley and tail pulley, and not touching the outer plates.

- Check oil level in the gear reducer, and follow gear reducer maintenance.

- Fitting on 3/4” flange bearing (Item #14 on parts list) should be greased at the same time (every 6-8 months) as changing the oil in the gear reducer.

- Check wiper blades for wear and proper setting. Reset adjustable wiper for proper wiping action if necessary.

- Abanaki Corporation recommends keeping a spare belt and a set of wiper blades in stock.

GEAR REDUCER MAINTENANCE

(SEE FIG. 8)

Use Abanaki Part #PGROIL

Oil Capacity is 3.1 ounces.

Change oil after first 6 months. Annually thereafter.

May operate at 205(F (96(C).

Top plug should be removed (if not already done from step 11A) and replaced with breather plug (furnished with reducer).

Bottom plug is for drain.

Center plug is oil level. Fill to this point.

Bottom plug and center plug are located below output shaft.

| ITEM | QTY | PART NAME | ITEM | QTY. | PART NAME | ITEM | QTY. | PART NAME | ITEM | QTY. | PART NAME |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | Main Base Weldment | 14 | 1 | 3/4” Flange Bearing | 27 | 1 | Tail Pulley Shaft | 40 | 2 | 1/4” Lock Washer |
| 2 | 1 | Head Pulley | 15 | 1 | 3/4” Shaft Collar | 28 | 3 | 3/8-16 x 1” Lg. Hex Hd. Bolt | 41 | 2 | 3/8” Fender Washer |
| 3 | 1 | Removable Cover Guard | 16 | 1 | Channel Mount Clamp | 29 | 2 | 3/8-16 x 1” Lg. Carriage Bolt | 42 | 10 | 1/4-20 x .50” Lg. Button Hd. |
| 4 | 1 | Discharge Trough Weldment | 17 | 1 | Support Gusset (Channel Mount) | 30 | 4 | 3/8-16 x 1.50” Lg. Hex Hd. Bolt | 43 | 1 | 1/4-20 x 2” Lg. Hx Hd Full Thd Bolt |
| 5 | 1 | Side Plate (Bearing) | 18 | 1 | Flat Mount Plate | 31 | 1 | 1/4-20 x 1.25” Lg. Hex Hd. Bolt | 44 | 1 | Hinged Wiper Ass’y Extn. Spring |
| 6 | 1 | Cover Plate | 19 | 1 | Flat Mount Discharge Trough | 32 | 2 | 1/4-20 x .75” Lg. Hex Hd. Bolt | 45 | 2 | 1/4-20 X .25” Lg. Set Screw |
| 7 | 1 | Head Pulley Shaft | 20 | 1 | Motor | 33 | 7 | 1/4-20 x .62” Lg. Hex Hd. Bolt | 46 | 2 | 3/16” x 3/16” x 3/4” Lg. Key |
| 8 | 1 | Gear Reducer | 21 | 2 | Wiper Insert | 34 | 7 | 3/8-16 Hex Nut | 47 | 1 | 1/4-28 X .25” Lg. Set Screw |
| 9 | 1 | Outside Wiper Blade Assembly | 22 | 1 | 8” Wide Belt | 35 | 3 | 1/4-20 Hex Nut |  |  |  |
| 10 | 1 | Inside Wiper Blade Assembly | 23 | 1 | Tail Pulley – Std. | 36 | 1 | 1/4-20 Locknut |  |  |  |
| 11 | 1 | Support Angle Spacer | 24 | 1 | Tail Pulley – High Capacity | 37 | 1 | Spring 3/8x3/4x.032 |  |  |  |
| 12 | 1 | Adjusting Cam | 25 | 1 | Yoke & Chain | 38 | 5 | 3/8” Flat Washer |  |  |  |
| 13 | 1 | Coupling Guard | 26 | 1 | Retainer/Yoke & Chain | 39 | 4 | 3/8” Lock Washer |  |  |  |

Copyright 2000 by ABANAKI CORPORATION. All rights reserved. No part of this work covered by copyright may be reproduced or used in any form or by any means without written permission of Abanaki Corporation.   Abanaki reserves the right to make changes to the Model 8( Oil Skimmer parts list at any time, without notice.

Note: (1)Parts list shows parts for flat & channel mounting. (2)All parts shown may not be standard. 04/00

# Text boxes

Model8-3_1.DOC

Figure 3

Figure 4

Figure 5

Figure 6

Figure 7

Model 8(

Oil Skimmer(

Parts List

Figure 2

Figure 1

Figure 8

Your Abanaki Oil Grabber( Skimmer has been manufactured and packaged to rigorous standards of design and service. Proper installation and maintenance of the unit is essential for efficient oil removal and long lasting use.

We have tried to make these instructions as clear as possible. If you have any questions, please call: 1-800-358-7546